Architetture dei Sistemi di Elaborazione 02GOLOV	Computer Architectures / 02LSEYG
Laboratory / 0x04	Expected delivery of lab_04.zip must include: / program_1.s, program_1_a.s, and program_1_b.s / This file, filled with information and possibly compiled in a PDF format.
Delivery date: / November 7th 2025

This lab will explore some of the concepts seen during the lessons, such as hazards, rescheduling, and loop unrolling. The first thing to do is to configure the GEM5 simulator with the Initial Configuration provided below:
INTEGER_ALU_LATENCY = 1
INTEGER_MUL_LATENCY = 1
INTEGER_DIV_LATENCY = 1
FLOAT_ALU_LATENCY = 4
FLOAT_MUL_LATENCY = 8
FLOAT_DIV_LATENCY = 20

Write an assembly program (program_1.s) for the RISCV architecture able to compute the output (y) of a neural computation (see the Fig. below):

x = sum from {j "="0} to {K "-"1} {{i} rsub {j} "*" {w} rsub {j} "+" b}
y = f(x)

      where, to prevent the propagation of NaN (Not a Number), the activation function f is defined as:

f left (x right ) "=" left lbrace stack { 0," "" ""&"if" "the" "exponent" "part" "of" "x" "is" "equal" "to" " 0x7FF # x," "" ""&"otherwise } right none

Assume the vectors i and w respectively store the inputs entering the neuron and the weights of the connections. They contain K=16 single precision floating point elements. Assume that b is a single precision floating point constant and is equal to 0xab, and y is a single precision floating point value stored in memory.
Compute y.

Given the Base Configuration, run your program and extract the following information.

	Number of clock cycles	Total Instructions	CPI (Clock per Instructions)
program_1.s	354	188	1.88298

    1. Optimize the program by re-scheduling instructions to eliminate as many hazards as possible. Manually calculate the number of clock cycles for the new program (program_1_a.s) to execute and compare the results with those obtained by the simulator.

    1. Unroll the program (program_1_a.s) two times; If necessary, re-schedule instructions and increase the number of registers used. Manually calculate the number of clock cycles to execute the new program (program_1_b.s) and compare the results obtained with those obtained by the simulator.

Complete the following table with the obtained results:

Program	program_1.s	program_1_a.s	program_1_b.s
Clock cycles by hand	352	333	254
Clock cycles by simulation	354	335	258

Collect the Cycles Per Instruction (CPI) from the simulator for different programs

	program_1.s	program_1_a.s	program_1_b.s
CPI	1.88298	1.78191	1.55422

Compare the results obtained in 1) and provide some explanation if the results are different.

Eventual explanation: I risultati variano per il riscaldamento delle cache e I 3 colpi di clock finali

    1. Try different unrolls for the program (program_1_a.s); If necessary, re-schedule instructions and increase the number of registers used. Manually calculate the number of clock cycles to execute the new program (program_1_b.s) and compare the results obtained with those obtained by the simulator.

Complete the following table with the obtained results:

Program	Number of Loop Unrolling	Code size [bytes]	Clock Cycles / [CC]
program_1_a.s		169	335
	2	265	258
	4
	8
	16

In order to calculate the code size of your program you can open in ./programs/you_program/your_program.dump file to retrieve the compiled disassembled code of your executable in which you have the effective addresses from which the code will be executed.

For example (on the right), for your_program you have your disassembled file on 32 bit addresses.